## Slide 1: SINET6 DDoS Mitigation Service
Naoya Kitagawa
National Institute of Informatics (NII), Japan
June 26-27, 2023

## Slide 2: Automatic DDoS Mitigation Service
Internet
Launched a new service that automatically detects and prevents DDoS attacks
  Operation as an official service started in January 2023
  Deployed a DDoS attack detection function within SINET
  Register IP addresses for attack detection based on service registrations
  Real-time DDoS attack detection and alerting
    Packet filter configurations can be automatically set about 10 seconds after an attack is detected (Under development)
Router
Router
Institution
❶ DDoS attack detection
❷ Application for mitigation
❸ Configure packet drop settings on the RR
❹ Configure filter settings on the routers
DDoS Mitigation Service
❶
❶ Service Application (Target IP Address Registration)
❷ Information collection
❸ DDoS attack detection
❹ Configure filter settings on the routers
❶
❷
❹
❸
Need more than several hours from application to completion of packet dropping setup
Approx. 10 seconds from attack detection to completion of packet dropping configuration
RR
Conventional Mitigation Service
New Mitigation Service
❷
Operator
SINET Reception Desk
Internet
❹
❹
❸
Operator
❶
Router
NEW！
Institution
SINET Reception Desk

## Slide 3: System Components
NTD
  The main element of the system that performs DDoS Attack detection on mirrored packets received from routers
  No direct manipulation of NTD in the system in operation
  No GUI; status is referenced via CMS
CMS
  Central Management System
  Used to change attack detection thresholds, change operation mode (Monitor, Mitigate), and manage system-wide alerts
SWA
  Provides GUI operation and information reference for this system
  Display the control status of the system, traffic graphs (pass/monitor/block), and attack information
  Provides IP address registration of the router to be controlled
SSP
  User portal
  Creates tenants and tenant administrator accounts
  Browses graphs and attack information for all created tenants

## Slide 4: Test System Configuration
master server
(HPE ProLiant
DL360 Gen 10)
eno3
eno4
eno1
eno5
eno6
(10G)
VM
(vNTD)
VM
(vCMS)
VM
(vSWA)
KVM
macvlan0
eno2
(10G)
dummy traffic generation server
(hping1 as source)
dummy traffic generation server
(hping2 as target)
management
NAT
(ip masquerade)
Actual traffic
(Mirror input)
Internet
PCI passthrough
Remote Control
(SSH, http, https)
hping1
hping2
nii-RM1
(MX960)
nii-RM2
(MX960)
nii-RM3
(MX480)
xe-5/0/0
eno2
eno1
enp1s0f0
mirrored
xe-5/2/0
xe-7/0/0
enp1s0f0
eno1
enp11s0f0
enp3s0f0
Private segment for server operation
Jump Server
SINET
eno2
.201
ssh
ssh
GUI (CMS)
GUI (SWA)
1G
1G
DDoS Mitigation System
mirrored
xe-5/0/1
ex4300
ex4300
(←same as
ex4300)
Not connected
(reserve)

## Slide 5: Test System Configuration (cont’d)
DDoS Mitigation System
Mirror xe-5/0/0 and
xe-5/0/1 to xe-5/0/2
hping1
xe-5/0/0
nii-RM1
(MX960)
nii-RM2
(MX960)
nii-RM3
(MX480)
xe-5/2/0
et-7/3/0
et-5/3/0
(down)
et-5/1/0
et-7/1/0
et-5/1/0
et-7/1/0
xe-7/0/0
et-5/3/0 (down)
et-7/3/0
et-5/1/0
et-4/3/0
(down)
et-5/3/0
ex4300
eno5
VM
(vNTD)
VM
(vCMS)
VM
(vSWA)
mirrored
telemetry
netconf
eno6
et-4/1/0
(down)
xe-7/0/1 (9/7 add)
mirrored
xe-1/1
xe-1/2
hping2
xe-5/0/1
ex4300
NII traffic
telemetry (Statistics collection)
Netconf (Filter setting/cancellation)
Mirror

## Slide 6: Processing flow in monitor mode
hping1
hping2
SWA
...
Transmission Start
(hping3 execution)
TCP SYN floods
Router (nii-RM1)
Stop Transmission
(hping3 stop)
Approx. 5 minutes
since last transmission
15-20 secs.
netconf
netconf
Detect the attack
Set up
additional filter
Filter Release Setting
telemetry packet (for Firewall filter)
user data packet (DDoS attacks)
telemetry
1send/sec
Filter is applied and only
monitoring is performed
Operation mode setting
(Monitor mode)
CMS
Continues to receive
packets after attack
detection
※ Router ->NTD mirroring is omitted.

## Slide 7
hping1
hping2
SWA
...
Transmission Start
(hping3 execution)
TCP SYN floods
Router (nii-RM1)
Stop Transmission
(hping3 stop)
Approx. 5 minutes
since last transmission
15-20 secs.
netconf
netconf
Detect the attack
Set up
additional filter
Filter Release Setting
telemetry packet (for Firewall filter)
user data packet (DDoS attacks)
telemetry
1send/sec
Operation mode setting
(Mitigation mode)
CMS
Block packet reception
upon attack detection
※ Router ->NTD mirroring is omitted.
Processing flow in mitigation mode
Packets are discarded
by the filter

## Slide 8: Example of automatic config submission to router (monitor)
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 19:21:05 JST
firewall {
family inet {
filter DDMON-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 19:13:06 JST
firewall {
family inet {
filter DDMON-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term e47a37ac4dc5a630bd7fc1f16d129f22-match {
from {
destination-address {
202.241.0.1/32;
}
packet-length 128-255;
protocol tcp;
ttl 64-127;
destination-port 1111;
tcp-flags "!fin & syn & !rst & !psh & !ack";
}
then {
count Corero-auto-e47a37ac4dc5a630bd7fc1f16d129f22-match;
port-mirror;
next term;
}
}
term e47a37ac4dc5a630bd7fc1f16d129f22-action {
from {
destination-address {
202.241.0.1/32;
}
packet-length 128-255;
protocol tcp;
ttl 64-127;
destination-port 1111;
tcp-flags "!fin & syn & !rst & !psh & !ack";
}
then {
count ddmon-auto-e47a37ac4dc5a630bd7fc1f16d129f22-accept;
accept;
}
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 17:52:26 JST
firewall {
family inet {
filter DDMON-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
Before TCP SYN flood transmission starts
Stop sending TCP SYN flood → After filter is released
Automatically submitted from SWA to router
(by netconf)
“Accept" is set for monitor mode
netconf
netconf
Start sending TCP SYN flood → After attack detection

## Slide 9: Example of automatic config submission to router (mitigate)
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 19:31:42 JST
firewall {
family inet {
filter CORERO-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 19:24:11 JST
firewall {
family inet {
filter DDMON-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term e47a37ac4dc5a630bd7fc1f16d129f22-match {
from {
destination-address {
202.241.0.1/32;
}
packet-length 128-255;
protocol tcp;
ttl 64-127;
destination-port 1111;
tcp-flags "!fin & syn & !rst & !psh & !ack";
}
then {
count Corero-auto-e47a37ac4dc5a630bd7fc1f16d129f22-match;
port-mirror;
next term;
}
}
term e47a37ac4dc5a630bd7fc1f16d129f22-action {
from {
destination-address {
202.241.0.1/32;
}
packet-length 128-255;
protocol tcp;
ttl 64-127;
destination-port 1111;
tcp-flags "!fin & syn & !rst & !psh & !ack";
}
then {
count ddmon-auto-e47a37ac4dc5a630bd7fc1f16d129f22-discard;
discard; ★
}
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
{master}
nii@nii-RM1> show ephemeral-configuration ddmon
## Last changed: 2020-07-21 19:21:05 JST
firewall {
family inet {
filter CORERO-MITIGATE {
term egress_manual {
then next term;
}
term discard_manual {
then next term;
}
term discard_auto {
then next term;
}
term accept_manual {
then next term;
}
term accept_auto {
then next term;
}
}
}
}
{master}
nii@nii-RM1>
discard" is set for mitigation mode
netconf
netconf
Before TCP SYN flood transmission starts
Stop sending TCP SYN flood → After filter is released
Start sending TCP SYN flood → After attack detection
Automatically submitted from SWA to router
(by netconf)

## Slide 10: Service Configuration
corero-master
(HPE ProLiant DL360 Gen 10)
eno3
eno4
eno1
eno5
eno6
(10G)
VM
(vNTD)
VM
(vCMS)
VM
(vSWA)
KVM
macvlan0
eno2
(10G)
NAT
(ip masquerade)
PCI passthrough
ssh
(CMS) https://192.168.0.201
(SWA) https://192.168.0.202:8000
(SSP) https://192.168.0.204
DDoS Mitigation System
nii-RM1
(MX960)
nii-RM2
(MX960)
nii-RM3
(MX480)
SINET
tokyo1-GM2
tokyo1-GM
VM
(vSSP)
ex4300
xe-0/2/0
vlan300
(untag)
telemetry
netconf
Mirror
(1:1000)
ge-0/0/13
Mirror
(1:1000)
xe-4/0/0.0
enp11s0f0
enp3s0f0
Jump Server
ssh
ge-0/0/21
Incoming telemetry packets (30000/udp) to SWA
xe-1/0/0:1.400
ae2.1002
200G
mirrored
Incoming 443/tcp packets to vSSP (for access to SSP)
disabled
et-9/0/2.0
100G
ae4.0
20G
mirrored
Remote Control
(SSH, http, https)

## Slide 11: Threshold and Rate Limit
If the traffic matching the condition exceeds the threshold, all such traffic is subject to blocking.
Threshold
Allowed up to Rate limit even if detection condition is met.
Only the amount exceeding the rate limit is blocked.
Threshold
Rate Limit
pps or bps
pps or bps
Two types of parameters for each detection rule: “Threshold” and “Limit”
  Packet Threshold (pps), Bit Threshold (bps)
    Rule application threshold (traffic matching the condition and exceeding the threshold is subject to detection)
  Packet Rate Limit (pps), Bit Rate Limit (bps)
    Allowable rate of transit for rule-matching traffic (even detection targets are allowed to pass up to a certain amount)

## Slide 12: Confirmation of Attack Detection Results
Institution's administrators can access the service portal to view real-time attack detection results from the DDoS Mitigation service
...
DDoS Mitigation
System
Monitoring
Results
Administrator 1
(Tenant Admin)
Administrator 2
(Tenant User)
Service Portal
Access with browser
University/Institution
SINET
The Internet
Real-time DDoS attack detection
Automatic filter for DDoS attacks
Control
Control
Monitor
Monitor

## Slide 13: Information available on the portal site
Graphical display of traffic volume
  Graph of the amount of traffic received by each institution's network over time
  Graphical display of the amount of discarded DDoS attack traffic is also supported
Display of IP addresses of frequent attack targets
  Ranking of the most frequently attacked IP addresses in the institution's network
List of detected attacks
  List of detected DDoS attacks
  Target IP address of attack, detection period, amount of detected traffic, etc.
x.x.x.x
List of detected attacks
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
IP addr. of frequent targets
Traffic amount
Graph of traffic volume for each attack
・Browser-based information display
・E-mail report function
・Login User Management

## Slide 14
Narrow down the display target
by entering CIDR
Traffic Volume Graph
Automatically blocked attack traffic
volume can also be displayed
(Automatic block control is under development)
IP address ranking of attack targets
List of detected attacks
(Target IP address, date and time of the attack, reason for detection, etc.)
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
AAA学部
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
xxx.xxx.xxx.xx
XX研究室
XX研究室
YY研究室
AAA学部
AAA学部
YY研究室
AAA学部
ZZセンター
BBBグループ
Provides traffic graph and attack detection list
Overview
Narrow down the time period to display
（ Last 24 hours by default）
Detection Status
(Under Attack or not, etc.)

## Slide 15
Click the "+" icon from the attack list to display the traffic graph
Print (Browser function)
Narrow down the attack detection results to be displayed
・IP address
IP address of the attack target
・Attack ID
ID for attack identification
・Asset Name
Subnet name as defined by the institution's admin
・Asset Group
Subnet group name as defined by the institution’s admin
Narrow down the time period to display
（ Last 24 hours by default）
Analysis
Provides information on detected DDoS attacks
Traffic graphs for individual attacks can be viewed

## Slide 16
Attack Detection List
Extracts and lists attack information for registered IP addresses
① IP addresses targeted by the attack
② Attack summary (TCP PSH/ACK Flood, UDP Reflection, etc.)
③ Services targeted by the attack (protocol, port number, etc.)
Asset Group | Asset Name | Target IP | Attack Status | Start time | Duration | Peak [Mbps] | Attack Volume | Description
Faculty of Engineering | Suzuki Lab. | 130.xx.xx.xx | Ongoing | 06/15/21 14:25:38 | 00:02:00 | 90 | 92GB | UDP Reflection from https (443/udp) to service 56xxx 57xxx
Faculty of Science | Sato Lab. | 130.xx.xx.xx | Completed | 06/15/21 11:10:05 | 00:01:00 | 37 | 19GB | TCP PSH/ACK Flood to service http-alt (8080/tcp)
1
2
3
Can be displayed with the actual group name if the administrator of
each institution registers the name in advance

## Slide 17
日時指定(From,To)で
表示期間絞り込み可能
(※デフォルトは直近24時間指定)
CIDRで表示対象絞り込み可能
Institutional administrators can further subdivide the applied network addresses and name or group the divided address blocks
The network segment to which the IP address under attack belongs can be displayed and sorted on the “Overview” and “Analysis” screens using the defined name
Monitored CIDR management (Assets)
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
Other than above
(Undefined)
Sato Lab.
Suzuki Lab.
XTZ Center
(No Name)
Fac. of Eng.
ABC Group
(No Name)
(Example)
Registered CIDR
192.168.0.0/16
Asset Name
Asset Group
Fac. of Sci.

## Slide 18: Conclusion and Future Tasks
<Conclusion>
DDoS Mitigation Service was launched as an official service in January 2023 after operational verification
29 institutions are using the new service, as of June 25, 2023
Currently in development to add packet drop function, which will be available upon completion
<Future Tasks>
Considering a method to evaluate the attack detection accuracy of the system
  It is difficult for us to know if detected attacks were actually observed at each institution
  Get feedback on regular user surveys?
Tuning of attack detection thresholds and their maintenance is not easy, since the line bandwidth of institutions connected to SINET range from ~1G to 400G
  Set several thresholds for each line bandwidth institution → Need to adjust while continuously checking attack detection status